## Slide 1: L8.10 - Infrasound & Assignment 8.3

## Slide 2: Assignment #8.3
Implement a distance measuring system using the ultrasound sensor & OLED display in your kit:
  measure object distance from ~ 5 to 200 cm
  Continuously display distance to detected object in cm using your 4-digit, 7-segment display with 1 cm resolution
Due Saturday 5/10/25

## Slide 3
human hearing range:
20 Hz – 20,000 Hz (20 kHz)
Echo

## Slide 4
Speed of sound:
343 m/s
741 mph
1,125 ft/s
speed of light:
300,000,000 m/s
983,571,056 ft/s

## Slide 5: Ultrasonic SONAR
bats, dolphins “see” (navigate) using sound waves above 20KHz
HC-SRO4 is a 40 KHz SONAR

## Slide 6
Ultrasonic Distance Sensor HC-SR04
& ATmega328P
object
distance R
10 us
Trig
speed of sound: Vs = 343 m/s; 34,300 cm/s
tx waveform
echo signal
rx waveform
Echo
T=2R/Vs
sensor creates an echo pulse of width T = 2R/Vs Code measures time difference between rising & falling edge of pulse.
10 usec wide 5V pulse provided to trigger the sensor via a GPIO output pin
sensor transmitter emits a 40 KHz burst of sound. Bounces off target and returns to sensor receiver 2R/Vs seconds later
Tx
Rx

## Slide 7
Echo
T=2R/Vs
Speed of sound: Vs = 343 m/s = 34300 cm/s = 34300 x 10-6 cm/uS = 0.034 cm/uS
echo pulse width T = 2R/Vs
# Timer clock tics at 64 uSec per tic
Example: R = 10 cm; T = 2*10/0.034 = 588 uS

## Slide 8
8
Timer/Counter
pre-load timer with 0x00
apply clock
Counter Register will count up
Arduino Uno board has 16 MHz Clock
clkIO = 16,000,000 cycles/second; 0.0625 uSec/cycle
clk/8 = 2,000,000 cycles/second, 0.5 uSec/cycle
clk/64 = 250,000 cycles/second, 4 uSec/cycle
clk/256 = 62,500 cycles/second, 16 uSec/cycle
clk/1024 = 15,625 cycles/second, 64 uSec/cycle
0x00

## Slide 9
(Echo) Sensor generates a pulse of duration T=2R/Vs
Let us measure the duration (width) of a pulse connected to a GPIO pin, for example PB1
start a timer counting (normal mode; 16 MHz clock/1024)
wait for the PB1 to go high
Tr = # clock cycles to the rising edge (close to 0)
wait for PB1 to go low
Tf= # clock cycles to the falling edge (between 0 and 182)
T = Tf - Tr
Speed of sound: Vs = 343 m/s = 34300 cm/s = 34300 x 10-6 cm/uS = 0.034 cm/uS

## Slide 10
(Trig) 10 us pulse triggers the ultrasound sensor
transmitter emits a 40 kHz sound wave pulse
Pulse echo is detected by the receiver; clock is stopped
delay time is
2R/Vs
(Echo) Sensor generates a pulse of duration T=2R/Vs
time
Speed of sound: Vs = 343 m/s = 34300 cm/s = 34300 x 10-6 cm/uS = 0.034 cm/uS
PORTB &= ~(1 << TRIG); // 5 usec pre-TRIG
_delay_us(5);
PORTB |= 1 << TRIG; // 10 us pulse
_delay_us(10); // to ultrasound
PORTB &= ~(1 << TRIG); // TRIG pin
while ((PINB & (1<<ECHO))==0); //wait till ECHO goes high
timeToRisingEdge = TCNT0;
while (!(PINB & (1<<ECHO))==0); //wait till ECHO1 goes low
timeToFallingEdge = TCNT0;
pulseWidth = timeToFallingEdge - timeToRisingEdge;
range = pulseWidth * 1.098; //one way distance to target in cm
void timer0_init(void){
TCCR0A = 0; //timer mode - normal
TCCR0B = 0x05; //1024 prescaler
}
#define TRIG PB0
#define ECHO PB1
#include <avr/io.h> (and other includes)
int main(void){
unsigned int timeToRisingEdge, timeToFallingEdge;
unsigned int pulseWidth;
float range;
timer0_init();
while(1){
send_to_monitor();
}
TCNT0 = 0;